What's the buzz about HORNET?

---
You've probably all seen the news…
- "Internet-scale anonymity"
- "Without sacrificing security, the network supports data transfer speeds of up to 93GBps"
- "can be scaled at little cost"
- "a better, faster Tor"

---
You've probably not read the abstract...
"We present HORNET, a system that enables high-speed end-to-end anonymous channels by leveraging next generation network architectures. HORNET is designed as a low-latency onion routing system that operates at the network layer thus enabling a wide rangeof applications. Our system uses only symmetric cryptography for data forwarding yet requires no per-ﬂow state on intermediate nodes. This design enables HORNET nodes to process anonymous trafﬁc at over 93 Gb/s. HORNET can also scale as required, adding minimal processing overhead per additional anonymous channel. We discuss design and implementation details, as well as a performance and security evaluation."

---
HORNET: High-speed Onion Routing at the Network Layer
- Low-latency onion routing network
  - Leverages the existing Sphinx onion routing protocol
- Geared towards speed and scalability
  - Use next-gen network gear instead of building an overlay

---
Desired properties
- Path information integrity and security
  - e.g. no tagging attacks
- No cross-link identification
- Session unlinkability
- Payload secrecy and end-to-end integrity
  - Adversary can only learn packet length and timing

---
Claims
- Better speed than existing onion routing networks
  - Tor, I2P
- Better security than existing (proposed) network layer anonymity networks
  - LAP, Dovetail

---
Speed

---
Security

---
Why is it fast?

---
Stateless data transmission

---
Stateless data transmission

---
Data packet header lengths
Scheme	Header Length	Sample Length (Bytes)
LAP	12 + 2s.r	236
Dovetail	12 + s.r	124
Sphinx	32 + (2r + 2)s	296
Tor	3 + 11.r	80
I2P	20	20
HORNET	8 + 3r.s	344
s = length of symmetric element
r = maximum AS path length
For sample length, s = 16 Bytes and r = 7

---
Gains
- No route lookup time
- No route storage
  - Tor stores at least 376 bytes per circuit
    - Requires almost 20GB of memory for a load level of 5 million new sessions per minute

---
Mostly symmetric crypto
- Each HORNET node performs one DH key exchange during setup phase
- Only symmetric operations used during data phase
  - 5% slower than LAP and Dovetail for small packets (64 bytes)
  - 71% slower for large packets (1200 bytes)

---
How?
- Decrypts setup packet
  - Sym key from medium/long-term DH priv key and sender's DH pub key
- Generate transient DH key
- Calculate a symmetric key from transient DH priv key and sender's DH pub key
- Encrypt routing info with local medium-term symmetric key
- Forward encrypted routing info + transient DH pub key
- Delete transient DH key

---
No replay protection
- Packet replay is ignored within the lifetime of a session
  - Leads to easy DoS
- They suggest that adversaries would be deterred by the risk of being detected by volunteers / organizations / ASs
  - but the detection process is going to add additional processing time and therefore compromise throughput

---
So is this the end of Tor and I2P?

---
Why not?
- Designed for new routing hardware that doesn't exist
- Only covers session setup and data transmission
  - Assumes routing state only shows next hop
  - Assumes the presence of path discovery
  - Assumes the presence of node discovery
- Can be used with upper-layer anonymity protocols for stronger security guarantees

---
It's actually very similar to I2P tunnels!
- Both use "non-interactive" telescopic tunnel building
- Both only use symmetric crypto for data transmission
  - Don't confuse I2P tunnels with I2P sessions
    - (But I2P sessions also use mostly-symmetric crypto via "session tags"…)
      - ((Yes, yes, this gets confusing...))

---
Key difference between HORNET and I2P
- I2P tunnel packet headers are smaller than HORNET
  - But I2P pads all to 1024 bytes
- I2P stores routing data
- I2P uses a bloom filter to detect packet replay
- I2P has a higher-level end-to-end crypto layer

---
Key points
- It doesn't actually exist
  - You can't throw away Tor and I2P just yet ;)
- It's only one piece of the puzzle
- Speed has trade-offs
- It's still a good idea!

---
Fun aside (if we get time):
Implementing HORNET in I2P

---
Discussion time :)